100-50-DS

Modular Slide-In CAFSystem

This unit shall be a slide-in, modular, portable compressed air foam unit designed and constructed to discharge water, foam solution or compressed air foam. The system develops a minimum of 80 GPM of water at 125 PSIG (379 L/min @ 6.9 bar) and 40 CFM of air at 125 PSIG (1.13 m3/min @ 8.6 bar). The 100-50-DS also features compressed air for pneumatic tools and can pump water or air independently. The unit shall come with a Rand 50 sCFM compressor, and Aquis™ 1.5 foam proportioner, and electric auto-sync balancing system. It shall be available with an optional Operator Interface Terminal (OIT).

This unit shall come with a CPD-2 centrifugal water pump utilizing an aluminum case, double-hubbed bronze impeller, stainless steel shaft and maintenance-free mechanical seal. It shall come with a 3 inch NPT intake and 
2 inch discharge. It shall come with a Venturi Primer with electric activation switch and a poly chain drive transmission with an automatic tensioner and 8mm pitch sprockets.

The unit shall be powered by a Deutz engine, model D2011L02i, two-cylinder, air / oil cooled, delivering a maximum of 30 horsepower (22.5 kW), four-cycle, diesel fueled. The engine shall come with a two (2) year manufacturer’s warranty. The engine shall draw fuel from a fuel tank (not supplied) via a pulse fuel pump. There shall be a pressure lube system with spin-on oil filter. An extension hose is installed on the engine oil drain with a valve located at the oil pan and a plug installed in the end of the hose to facilitate oil changes. It shall come with a 12 or 24-volt electric with 40A alternator, electric ignition and start switch along with a spark arrestor muffler. 
The frame of the unit shall be made of high-strength, stainless steel.

The unit shall come with an oil-filled, rotary screw air compressor, sized to supply a minimum of 50 scfm 
(1.4 m3/min) of usable air. The unit shall come with an air compressor is controlled by the pneumatic modulation inlet valve mounted on the air end. It shall control air delivery while maintaining constant pressure. The unit shall come with an auto sync balancing system which automatically maintains the air pressure within +/- 5% of the water pump pressure throughout the pressure range. The auto sync balancing system is located on the operator’s panel and allows for the following modes:

- Automatic – Air pressure matched to water pressure

- Fixed – Air pressure defaults to manual setting on compressor mounted control valve

- Unload – Air pressure reduced to 40 psig (2.8 bar) for standby operations

Page 1 of 2

The unit shall come with a spin-on, full-flow oil filter unit is part of the system to control oil flow to the cooler. All lines are routed in braided hose conforming to SAE 100R1 standards for hydraulic hose. The unit shall be available with a modular air / oil separator. The unit shall be available with an air compressor cooling system. The air compressor shall be cooled by a 12 or 24 V electric / air fan type cooler. The system maintains recommended operating temperatures throughout the full operational range in ambient temperatures up to 115°F (46.1° C)

All air hoses, fittings and piping with the unit are rated to a minimum of 250 psi (17.5 bar). Air line fittings are constructed of brass, bronze or steel. Stainless steel or brass check air valves are utilized at all air injection points to prevent water back flow into the air lines. All hoses shall be secured to the frame with insulating clamps and located away from any heat sources.

The unit’s plumbing shall come with inlet piping 2 inch stainless steel pipe controlled with the pump panel. An inline strainer is provided. A 2 inch valve is provided behind the pump panel for overboard pump inlet with a 1.5 inch M-NST connection. Victaulic-type couplings are utilized in the pump inlet for flexibility and improved serviceability. The unit shall have plumbing to two panel mounted 1.5 inch discharge outlets incorporate a stainless steel manifold, welded stainless steel pipe and/or Class 1 high-pressure hydraulic hose with stainless steel fittings. 
A 1 inch tank fill provision with 1 inch is provided. Victaulic-type couplings are utilized in the discharge plumbing for flexibility and serviceability. All discharge plumbing is designed and tested to a minimum of 500 psig (34.5 bar) burst pressure. The unit shall come with panel mounted drain valves are provided to drain water from the water pump, discharge manifold and compressor colder.

The unit shall come with an Aquis™ 1.5 foam proportioner with Operator Interface Terminal (OIT), pump module with electric motor/motor driver and microcontroller unit, foam concentrate strainer, shielded electrical cables for connection for all electronic components, foam inject check valve, WYE strainer and flowmeter and tee.

125 Hardman Avenue South, South St. Paul, Minnesota  55075-2456 USA (651) 450-5000

Page 2 of 2

# Text boxes

Document Number	 Issue Date	  Rev. Date

F-2852	  07/18

Preferred Specifications